## Slide 1: Welcome to the Wireless World
Day 5: Bluetooth, BLE, and smartphone robot control
RoboLink | Grade 7-8
Phone -> wireless signal -> robot
PHONE
->
BLE
->
ROBOT

## Slide 2: Today's Mission
1
Decode
communication engineering
2
Connect
Bluetooth and BLE
3
Configure
HC-05 BLE and AT mode
4
Compete
today's robot race
Big idea: wireless communication is still communication engineering.

## Slide 3: What Is Communication Engineering?
Communication engineers design:
- devices that send and receive messages
- signals that travel through air, wires, or light
- ways to reduce mistakes from noise and interference
- rules so devices understand each other
Examples
Text message
Wi-Fi video call
TV remote
RoboLink phone app
Same job every time: move a message clearly enough that the destination can use it.

## Slide 4: A Basic Communication System
Source message starts
->
Transmitter message -> signal
->
Channel signal travels
->
Receiver detects signal
->
Destination message is used
The channel can change the signal.
distance, walls, interference, and noise
Engineers measure capacity, delay, and errors.

## Slide 5: Our Robot Communication System
Phone app command byte
->
BLE radio wireless
->
HC-05 BLE receives data
->
UART wires TXD/RXD
->
Arduino chooses action
->
Motors robot moves
Command map
1 = Stop 2 = Forward 3 = Backward 4 = Left 5 = Right
Lab connection
Module TXD -> Arduino D10 Arduino D11 -> module RXD through a voltage divider

## Slide 6: What Is Bluetooth?
- uses radio waves instead of wires
- works over short distances, usually across a room
- uses the 2.4 GHz radio band
- sends data in small packets using agreed rules
- connects phones, headphones, keyboards, sensors, and robots
Bluetooth
short-range wireless link
Bluetooth is not the internet. It is the short wireless link between nearby devices.

## Slide 7: Why Is It Called Bluetooth?
The name comes from a real historical king, not from a blue phone icon.
Harald "Bluetooth" Gormsson
- King of Denmark and Norway more than 1,000 years ago
- remembered for uniting groups of people
- engineers wanted their radio link to unite different devices
- the name started as a code name and stayed
H + B
The logo combines old runic letters for H and B.
H = Harald B = Bluetooth

## Slide 8: Two Bluetooth Paths: SPP and BLE
SPP: Serial Port Profile
- acts like a wireless serial cable
- common in older Bluetooth Classic robot projects
- sends a stream of bytes after pairing
BLE: Bluetooth Low Energy
- designed for low-power devices and sensors
- uses services and characteristics
- good for short robot control messages
Classic Bluetooth SPP stream
->
BLE services + bytes
Our classroom module and app use BLE.

## Slide 9: SPP: A Wireless Serial Cable
SPP is the style many classic HC-05 tutorials use.
Easy mental model
USB serial cable without the cable
- Arduino sends and receives characters
- phone app opens a serial connection
- good for simple terminal apps
Important for today
- Standard HC-05 modules are usually Bluetooth Classic SPP modules.
- Our classroom board is an HC-05-style BLE edition.
- When online tutorials disagree with the lab sheet, follow the lab sheet.
SPP = Serial Port Profile

## Slide 10: BLE: Bluetooth Low Energy
- devices can advertise: "I am here"
- a phone can scan and connect
- data is organized into services and characteristics
- great for sensors, beacons, fitness bands, and robot commands
- uses less energy than keeping a large data stream open all the time
Our BLE command idea
1
Stop
2
Forward
3
Backward
4
Left
5
Right
The app sends one byte. The Arduino decides what the byte means.

## Slide 11: Meet the HC-05 BLE Module
HC-05 BLE
TXD RXD VCC GND KEY/EN for setup
HC-05-style BLE edition
What it does
- receives a Bluetooth/BLE radio signal from the phone
- turns wireless data into UART serial data
- sends bytes to Arduino through TXD and RXD pins
- lets the robot be controlled without USB
Normal race mode = data mode
Setup = AT mode

## Slide 12: HC-05 Specs to Know
Radio
2.4 GHz Bluetooth radio with built-in antenna
Serial
UART TXD/RXD pins Lab baud: 9600
Logic
Protect module RXD with a voltage divider
Modes
Normal data mode and AT command mode
Common classic HC-05 datasheets list Bluetooth v2.0+EDR, SPP, 3 Mbps modulation, typical -80 dBm sensitivity, and up to +4 dBm transmit power.

## Slide 13: Master and Slave
These words describe who starts and controls a Bluetooth link.
Classic Bluetooth wording
- Master starts or controls the connection.
- Slave waits to be found and connected.
- Many HC-05 AT commands use ROLE=1 for master and ROLE=0 for slave.
Master -> Slave
Newer BLE wording
- Central usually scans and connects. The phone is often central.
- Peripheral advertises and waits. The robot module is often peripheral.
- Same idea, more modern terms.
Phone central -> module peripheral

## Slide 14: What Is AT Mode?
In normal data mode:
- phone commands go straight to the Arduino
- the robot can drive
- the module acts like a wireless cable
In AT mode:
- the module listens for text commands that begin with AT
- we can read or change module settings
Useful AT questions
AT
Are you alive? -> OK
AT+VERSION?
Firmware version
AT+NAME?
Module name
AT+ADDR?
Bluetooth address
AT+ROLE?
Master/slave role
AT+UART?
Serial baud settings

## Slide 15: How to Access AT Mode
1
Disconnect the phone/app from the module.
2
Power off the module or Arduino.
3
Hold the KEY/EN button, or connect KEY/PIO11 high as your board requires.
4
Power on while KEY/EN is active. A slow LED blink usually means command mode.
5
Connect TX/RX through a USB-serial adapter or an Arduino pass-through sketch.
6
Open Serial Monitor at the AT baud rate, often 38400 or 9600, with Both NL & CR.
7
Send AT. If the module replies OK, you are in AT mode.
Safety: do not send Arduino 5V directly into a 3.3V logic RXD/KEY pin.

## Slide 16: Lab Path: Test First, Then Drive
A robot race is easier when the communication link is already proven.
Part 1: Wireless command test
- phone sends one command
- module passes it to Arduino D10/D11
- Arduino prints it in Serial Monitor
- built-in LED turns on/off as a quick proof
Goal: prove wireless messages arrive correctly
Part 2: RoboLink control
- same commands now control the L9110 motor driver
- TouchDown sends movement command
- TouchUp sends 1 so the robot stops
- motor speed can be tuned if the robot drifts
Goal: control motion safely and reliably

## Slide 17: Robot Race Today
Race mission
- connect the phone to your team robot
- drive through the course without touching the robot
- use controlled moves, not full-speed guessing
- fastest clean run advances in the cup
Race rules
- one driver at a time
- hands off the robot during the run
- reset only from the start line
- if Bluetooth disconnects, stop and reconnect before retrying
- respect other teams' space and wiring
Engineering target: reliable control beats random speed.

## Slide 18: 7-Group Race Cup
Stage | Match | Team A | Team B | Winner
Round 1 | A | Group 1 | Group 2 | 
Round 1 | B | Group 3 | Group 4 | 
Round 1 | C | Group 5 | Group 6 | 
Bye | - | Group 7 | Advances | Group 7
Semifinal | SF1 | Winner A | Winner B | 
Semifinal | SF2 | Winner C | Group 7 | 
Final | F | Winner SF1 | Winner SF2 | 
Champion | - | Winner F |  | 
Option: draw group numbers randomly before the race if you want fair seeding.

## Slide 19: Exit Ticket
1
In our robot system, what is the source and what is the destination?
2
What part of the system is the channel?
3
How is BLE different from SPP?
4
What does AT mode let us check or change?
One-sentence summary: Wireless control works when every part of the communication chain works.

## Slide 20: Instructor Sources
- Bluetooth name origin: https://www.bluetooth.com/about-us/bluetooth-origin/
- Bluetooth LE primer: https://www.bluetooth.com/bluetooth-le-primer/
- Bluetooth Serial Port Profile page: https://www.bluetooth.com/specifications/specs/spp-1-2-html/
- SPP definition reference: https://community.infineon.com/t5/Knowledge-Base-Articles/FAQs-on-Bluetooth-Serial-Port-Profile-SPP/ta-p/915028
- HC-05 datasheet copy: https://components101.com/sites/default/files/component_datasheet/HC-05%20Datasheet.pdf
- Local Day 5 labs: Lab5_Part1_Wireless_World.ino and Lab5_Part2_RoboLink.ino
- Local AT sketch: Labs/AT_test/AT_test.ino
Instructor note: standard HC-05 modules are usually Classic/SPP; this course uses an HC-05-style BLE edition.

## Slide 21: Thank You
Good luck in the RoboLink race.